## Slide 1
Digital Twin
Household Energy Forecasting
TTM + PINN + Conformal Prediction + ADWIN Drift Detection
Team Members
Manan Velani (U23CS027)
Dharav Bodat ( U23CS049)
Om Amin (U23CS076)
Nikhil Chhasiya (U23CS022)
UCI Household
Power Consumption
2006 – 2010 • 2.07M Records • 1-Minute Resolution
7
Sensor Channels
~1.25%
Missing Values
3
Models Benchmarked
Department of Computer Science & Engineering • SVNIT Surat

## Slide 2
Problem Statement & Motivation
The Problem
Household energy consumption is inherently non-stationary with strong daily & seasonal cycles
Precise short-term forecasting (60-minute horizon) is critical for smart grid load balancing
Traditional models fail to capture physics laws (energy conservation) alongside data patterns
Sensor drift and concept shift over time degrade model accuracy in production
Why It Matters
⚡
Energy efficiency: accurate forecasting reduces wastage and lowers CO₂ emissions
📡
Smart meters generate terabytes of data — scalable ML pipelines are essential
🏭
Industrial digital twins require uncertainty-aware, physics-consistent predictions
🔄
Adaptive models that detect drift ensure reliability over multi-year deployments
🎯 Goal: Build a physics-informed, uncertainty-aware, drift-adaptive forecasting system for residential energy consumption

## Slide 3
Exploratory Data Analysis
🕗
Peak Hours
Energy peaks 18:00–21:00 daily (evening appliance use). Lowest consumption 03:00–06:00.
❄
Seasonal Pattern
Winter months (Dec–Feb) show significantly higher GAP, driven by heating. Strong annual cycle detected.
📅
Weekend Shift
Weekends (Sat–Sun) show higher daytime base load — occupants home; weekday mornings are low.
📈
Stationarity
ADF test: p < 0.05 → Stationary at macro level. KPSS confirms dual seasonality (daily + annual).
🔗
Lag Correlation
Strongest ACF peaks at Lag 24 (same hour −1 day) and Lag 168 (same hour −1 week).
Avg. Power by Hour of Day (kW)
Chart: 
| 0h | 1h | 2h | 3h | 4h | 5h | 6h | 7h | 8h | 9h | 10h | 11h | 12h | 13h | 14h | 15h | 16h | 17h | 18h | 19h | 20h | 21h | 22h | 23h
GAP (kW) | 0.9 | 0.7 | 0.65 | 0.62 | 0.63 | 0.75 | 1.1 | 1.5 | 1.6 | 1.45 | 1.4 | 1.35 | 1.3 | 1.25 | 1.2 | 1.3 | 1.6 | 1.9 | 2.15 | 2.2 | 2.1 | 1.9 | 1.6 | 1.2
Feature Correlation Highlights
Feature Pair | Correlation
GAP ↔ Global_intensity | ≈ 1.00 (dropped)
GAP ↔ Sub_metering_3 | ≈ 0.62 (strongest)
GAP ↔ Voltage | ≈ −0.21 (weak negative)
GAP ↔ Sub_metering_1 | ≈ 0.15

## Slide 5
Dataset Description
2.07M
Total Records
1 min
Granularity
4 yrs
Duration (2006–2010)
7
Sensor Features
~1.25%
Missing Values
Feature Columns
Feature | Unit | Description
Global_active_power ★ | kW | Total active power consumed (TARGET)
Global_reactive_power | kW | Reactive power (lag/lead)
Voltage | V | Mains supply voltage
Global_intensity | A | Avg current intensity (dropped — collinear)
Sub_metering_1 | Wh | Kitchen appliances
Sub_metering_2 | Wh | Laundry room
Sub_metering_3 | Wh | HVAC / Water heater (strongest predictor)
Source
UCI ML Repository
(Household Power Consumption)
Target Variable
Global_active_power (kW)
Key Insight
Global_intensity dropped (perfectly collinear with GAP).

## Slide 6
Data Preprocessing
1
Ingest & Parse
Load .txt (semicolon-delimited), parse Date+Time → DatetimeIndex. Reindex to full 1-min range to expose gaps. Cast all to float32.
2
Physical Validation
Negative Global_active_power → NaN. Voltage outside [220V–255V] → NaN. Compute E_rem = GAP×(1000/60) − S1 − S2 − S3.
3
Hierarchical Imputation
Short gaps (<30 min): cubic interpolation. Long gaps: seasonal fill from hour×weekday means. Finally ffill/bfill as safety net.
4
Outlier Treatment
IQR clipping (1.5×IQR) for GAP, Voltage, Global_intensity. Extremes are capped — not dropped — as high-load events are real.
5
Scaling
MinMaxScaler for all power/energy columns. StandardScaler for Voltage only. Applied fit-on-train, transform-on-test to prevent leakage.
6
Train / Val / Test Split
Temporal (no shuffle): 70% Train → 15% Validation → 15% Test. Split index preserves chronological order across all models.

## Slide 7
Methodology — Models & Architecture
Feature Engineering
E_rem:
Kirchhoff remainder energy (physics constraint)
hour/month/weekday sin-cos:
Cyclical encoding (prevents discontinuity at midnight/year boundary)
Lag-1, Lag-60, Lag-1440:
1-min, 1-hour, 24-hour autoregressive features
Rolling mean/std (60m, 1440m):
Short & long-term volatility signal
TinyTimeMixer (TTM) Architecture — IBM NeurIPS 2024
1.
PatchEmbedding → projects windows of length 8 into d_model=64
2.
2× MixerBlock → time-mix MLP + feature-mix MLP (GELU + Dropout)
3.
MultiHeadAttention (4 heads) with stored weights for XAI
4.
5-output head [GAP, S1, S2, S3, E_rem]
Seasonal Naïve (CP-2a)
Predicts y[t] = y[t−1440] (same minute yesterday). Provides MASE denominator for relative metric.
SVR — RBF Kernel (CP-2b)
GridSearchCV (C, γ) via 3-fold TimeSeriesSplit. Flattened sliding window as input. Benchmark from Aurangzeb et al.
TTM + PINN Loss (CP-2c/3)
L = 0.85 × MSE_data + 0.15 × Physics_loss. Physics: (GAP×1000/60 − S1−S2−S3−E_rem)²
Conformal Prediction (CP-4a)
Memory-efficient split conformal: q_hat from val residuals. Target ≥95% coverage. No full matrix allocation.
ADWIN Drift Detection (CP-4b)
Streams residuals to ADWIN (δ=0.002). On drift: trigger 3-epoch TTM fine-tuning + detector reset.
Config: window=168 | horizon=60 | batch=256 | lr=1e-3 | epochs=30 | patience=5 | AdamW + CosineAnnealingLR

## Slide 8
Results & Evaluation
RMSE
Root Mean Squared Error — penalises large spikes
MAE
Mean Absolute Error — avg deviation in kW
MASE
MAE / Naïve MAE — MASE < 1.0 beats baseline
RRA-Dir
Ramp direction accuracy — correct sign of Δy?
RRA-Mag
Ramp magnitude accuracy — 1 − error / naïve ramp
Model Performance Comparison
Model | RMSE (kW) | MAE (kW) | MASE | RRA-Dir | RRA-Mag
Seasonal Naïve | — | Baseline | 1.000 | — | —
SVR (RBF) | 0.391 | 0.278 | 0.824 | 71.2% | 0.683
TTM + PINN ★ | 0.298 | 0.211 | 0.625 | 78.9% | 0.742
Chart: RMSE & MAE by Model
| Seasonal Naïve | SVR (RBF) | TTM + PINN
RMSE (kW) | 0.55 | 0.391 | 0.298
MAE (kW) | 0.337 | 0.278 | 0.211
Chart: MASE (lower = better; <1.0 beats naïve)
| SVR (RBF) | TTM + PINN
MASE Score | 0.824 | 0.625
★ TTM + PINN achieves best scores across all metrics. Conformal predictor delivers ≥95% empirical coverage on test set.

## Slide 9
Comparison with Reference Paper
Reference: Aurangzeb et al. — King Saud University Journal of Engineering Sciences
"Short-Term Power Load Forecasting Using Deep Learning Approaches" — SVR with RBF kernel identified as optimal classical method (Table 3). Paper benchmarks LSTM, CNN, SVR on UCI dataset.
Aspect | Aurangzeb et al. (Reference) | This Work (Ours)
Best Model | SVR (RBF Kernel) | TTM + PINN (Foundation Model)
Architecture | Classical ML + 1-layer LSTM | PatchEmbedding + MixerBlocks + MHA
Physics Constraint | None | PINN Energy-Balance Loss (w2=0.15)
Uncertainty Output | Point forecast only | 95% Conformal Prediction Intervals
Drift Handling | Static model | ADWIN drift detection + adaptive fine-tuning
MASE vs Naïve | ~0.84 (reported) | 0.625 ↓ (−25.6% improvement)
XAI / Explainability | None | SHAP GradientExplainer + Attention Rollout
Feature: E_rem | Not present | Kirchhoff balance feature engineered
✅ Our system extends the reference by adding physics-informed training, conformal uncertainty bands, real-time drift detection, and XAI — all absent from the reference paper.

## Slide 10
Challenges, Limitations & Future Work
Challenges Faced
MAPIE matrix OOM crash: full [N×W×F] matrix = 12.1 GB → replaced with memory-efficient batched conformal
ADWIN sensitivity: too-low delta triggered excessive false-positive drift events → tuned δ=0.002
Numba/NumPy incompatibility with SHAP GradientExplainer — required downgrade to NumPy 1.24.4
SVR scalability: flattened sliding window (168×58 features) too large for full training set → sampled 2,000 rows
Colab kernel instability with large datasets: used nrows=50,000 subset for development runs
Current Limitations
Single household — findings may not generalise to commercial/industrial meters
Multi-step forecast limited to 60-min horizon; longer horizons untested
PINN loss weights (w1=0.85, w2=0.15) fixed — not learned adaptively
No real-time streaming pipeline — batch inference only
Future Extensions
01
Multi-household federated learning with differential privacy
02
Replace fixed PINN weights with meta-learned adaptive balance
03
Deploy as real-time Kafka streaming pipeline
04
Extend horizon to 24h with encoder-decoder Transformer
05
Integrate weather API features (temperature, humidity)

## Slide 11
Conclusion & Key Findings
Best Model
TTM + PINN
Foundation model with physics-informed loss outperforms all baselines
MASE Score
0.625
37.5% lower error than seasonal naïve; 24.2% better than SVR (RBF)
Coverage
≥ 95%
Conformal intervals guarantee marginal coverage on held-out test set
Drift Events
ADWIN
Adaptive fine-tuning triggered on drift; model stays current over time
Key Takeaways
Physics-informed learning (PINN) reduces constraint violations and improves generalization beyond pure data-driven models
Feature engineering (E_rem, cyclical encodings, multi-scale lags) provides strong inductive bias — validated by SHAP & Attention Rollout
Memory-efficient split conformal prediction provides statistically rigorous uncertainty without incurring OOM on large datasets
Sub_metering_3 (HVAC/Water heater) confirmed as the dominant predictor — consistent with Aurangzeb et al. (2021) findings
Production-grade pipeline: automated drift detection, adaptive retraining, and interactive Plotly dashboard for operational monitoring
UCI Household Power Consumption • TinyTimeMixer + PINN + ADWIN + Conformal Prediction • SVNIT Surat